## Slide 1: Future perspectives for underground energy storage in slovakia
Underground Energy Storage IN THE DANUBE REGION
Ladislav Barkoci

## Slide 2
Demand for energy storage
Underground energy storage activities in Slovakia
Future challenges
Agenda

## Slide 3
NAFTA STORAGE OPERATIONS ACROSS EUROPE
1
Stogit
183
2
Storengy
121
3
NAM
76.4
4
Uniper
68.2
5
RAG
67.0
6
NAFTA
60.7
20 TWh
40.7 TWh

## Slide 4
Demand for Energy Storage

## Slide 5
Why we need more energy storage?
First intuitive answer – we need more energy storage in the future to cover flexibility of supply when replacing dispatchable fossil sources of electricity by intermittent renewable electricity sources
...but this is not a whole picture...
World electricity generation from 1971 to 2017 by fuel (TWh)
Source: IEA Statistics, www.iea.org
65%

## Slide 6
Future energy storage need – full perspective
If the share of electricity in energy mix is increased then covering the intermittency of renewable electricity sources is even more acute.
Moreover, fossil fuels currently cover majority of seasonal energy demand. This seasonality needs to be addressed as well.
World total final energy consumption by source from 1971 to 2017 by fuel (Mtoe)
Source: IEA Statistics, www.iea.org
Electricity currently accounts for less than 20% of worlds final consumption of energy.

## Slide 7
European seasonal natural gas demand
31%
8%
Underground natural gas storages store significant part of energy consumed in EU and are actively used to balance seasonality of energy demand
Source: IEA Statistics, www.iea.org
Source: GIE AGSI Storage Data, https://agsi.gie.eu/#/
Europe UGS working gas level (TWh)

## Slide 8: 02
Underground energy storage activities in Slovakia

## Slide 9
Sun Storage – first lesson
1
2
3
Laboratory research
Pilot plant
Results
Laboratory research confirmed that 10% of H2 should not cause issues in the reservoir
Some chemical / microbial reaction was expected
Storing of energy in form of H2 in the mixture with natural gas – 10% vol. H2
No H2S production
Microbial reaction occurred
H2 mixed with cushion gas
Pilot project
NAFTA specified and delivered compressor unit
Pilot operation confirmed technical feasibility of the concept
Source of picture: RAG

## Slide 10
Research of the large-scale energy storage in the form of hydrogen in the geological structures
Project goals:
Identifying, laboratory testing and modelling of the suitable geological objects in Slovakia for hydrogen storage, depending on specific geological conditions as well as the amount of hydrogen mixed with the natural gas
Developing of the methodology to guide candidates interested in field of the energy storage in the form of hydrogen. The methodology should answer which tests needs to be done to allow real physical storage

## Slide 11
Research of the large-scale energy storage in the form of hydrogen in the geological structures
Project structure
1
2
3
Main activities
Research of H2 impact to the geochemical, mineralogical and geological properties of the reservoir
Monitoring of microbial impacts
Modelling of the selected structure
Project partners
Consortium of three academic institutes of SAV
Main universities in Slovakia: STU Bratislava, UK Bratislava, UPJŠ Kosice
Industrial partner - NAFTA
The project applied for financial support from the call of long-term strategic research of the Ministry of Education of the Slovak Republic

## Slide 12
Research of the large-scale energy storage in the form of hydrogen in the geological structures
  Characterization of chemical processes of the reservoirs
  Monitoring of potential changes in rocks, structures due to the influence of H2
  Individual experiments will be carried out in the reactor, simulating real reservoirs conditions (temperature, pressure ...)
Source of pictures: DBI Leipzig 2014; BOKU IFA Tulln 2014
  Hydrogen impact to the geological integrity as well as to the cap rock
  Research of possible H2 reactions with the abiotic parts of the reservoir
  Complex analysis of macro components of the reservoir, their properties (porosity, permeability, structure, etc.) and micro components of the reservoir (minerals, gases, sedimentary organic matter, etc.)

## Slide 13
Research of the large-scale energy storage in the form of hydrogen in the geological structures
  Analysis of the microbiome composition of the underground hydrogen reservoir
  Each deposit (except salt caverns) contains a microbial community
  Understanding it may help to eliminate inappropriate microbial reactions, or to eliminate microbial reactions or may indicate that the reservoir is not suitable for storing the mixture under given conditions
  Research of microbial activity in pressure reactor simulating real reservoirs conditions
  Analysis of microbial activities that can potentially take place under real conditions
  Monitoring the impact of hydrogen for a change in microbial activities, with an impact on the resulting products
Source of pictures: DBI Leipzig 2014; BOKU IFA Tulln 2014

## Slide 14
Research of the large-scale energy storage in the form of hydrogen in the geological structures
  Analysis and modeling of thermo-hydro mechanical behavior of rocks and construction materials
  Investigation of thermo-hydromechanical properties of reservoir layer and cap rock
  Testing the impact of H2 on materials used in selected natural gas storages – focus on sealing materials, rubbers and cement

## Slide 15: 03
Future challenges

## Slide 16
Establish sound regulation on hydrogen content in the gas grid
Develop sustainable technology of hydrogen storage in porous rock storages
Align time frame of research with application of the climate policy
Research cooperation within Europe
Climate policy coordination within whole world
Future Challenges
„The secret of change is to focus all of your energy, not on fighting the old, but on building the new“
Socrates