## Slide 1
Underground energy storage, Danube Region – possibilities and European perspective, Budapest, 2019.12.04
Serge van Gessel
Introduction to Underground Energy Storage
European Research and Technology Perspective
Serge van Gessel
Senior Advisor Economic Affairs, TNO
Chairman Geo-Energy Expert Group EuroGeoSurveys

## Slide 2
Challenge: Decarbonizing heating (and cooling) sector:
European Workshop on Underground Energy Storage, Paris, 2019.11.07
Serge van Gessel
Half of all final energy consumed in Europe is used for heating/cooling
Heat demand continues to follow a seasonal pattern
Heat demand primarily fulfilled by fossil (85%) incl. underground gas storage

## Slide 3
Seasonal fluctuation gas demand (heating)
(EIA 2019)

## Slide 4
Share of UGS Capacity vs Primary Energy Consumption
(downloaded from ourworldindata.org, 2019, GIE-2019)
EU gas storage volume
  ca. 1132 TWh
  156 operational sites
EU primary energy consumption 2016
ca. 16.400 TWh
UGS ~ 7%
EU primary gas consumption 2016
  ca. 4.200 TWh
  UGS ~ 27%
coal
oil
gas
nuclear

## Slide 5
Challenge: Integrate renewable electricity generation:
Intermittent renewable capacity expected to grow drastically towards 2050
Fossil flexibility (e.g. power plants) transforming or phasing out (coal)
High shares of intermittent renewables will require flexibility beyond the capacity of surface electrical storage options

## Slide 6
Strong increase of intermittent RE (EU and Globally)
(Shell Sky Scenario, 2019)
RE-intermittent
RE-base
Base
Fos
RE
intermittent
RE
base
Base
Fossi flex
RE-Int
RE
bas
Base
Fossi flexible

## Slide 7
1 Jan
31 Jan
ca. 4 days
35 GW
Germany: ca. 60 GW installed capacity (comparable to Dutch renewable ambitions in 2050)
ca. 30.000 wind turbines
Wind and Solar production, DE-NL-DK, January 2018
(Energy-charts.de, Frauenhofer 2019, ENTSOE, www.energidataservice.dk)

## Slide 8
1 Jan
31 Jan
Fossil fuels mainly used as balancing capacity.
Electricity production Germany, January 2018
(Energy-charts.de , Frauenhofer, 2019)
Wind
(variable)
Fossil
(flex)
Base load

## Slide 9
Wind and Solar production, DE-NL-DK, January 2018
(Energy-charts.de, Frauenhofer 2019, ENTSOE, www.energidataservice.dk)
Regional weather patterns: wind peaks and gaps are largely overlapping
(NL and DK scaled to German wind capacity)
1 Jan
31 Jan

## Slide 10
Pumped Hydro Storage and Surface Electrical
(DOE Global Energy Storage Database)
Total PHS EU: ~ 0,5 – 1,0 TWh assuming 8 - 16 hrs average duration (0,1% of current UGS capacity)

## Slide 11
35 GW
1 day ~ 8.000 batteries
Compensate 1 day of wind in Germany with E-storage
(A back-of-the-envelope calculation …)
1 day: 35 GW x 24 hours = 840 GWh
>> 4 days = ca. 3 TWh
Tesla Battery Australia: 129 MWh
PHS Goldisthal: 8.480 MWh
or 100 PHS lakes

## Slide 12
Large-scale Underground Energy Storage supports Europe’s ambitions for clean, secure and affordable energy:
Scalable low-carbon or zero-carbon flexibility solutions, proven
Applies to direct heat, gases and electricity
Conversion (e.g. Power-to-gas) > sectorial integration
Integrated with other (surface) flexibility options

## Slide 13
Flexibility Options
Regulated
Production
Demand
Response
Energy Import & Export
Energy
Storage
1.
2.
3.
4.
+ Conversion

## Slide 14
Family of Energy Storage Technologies

## Slide 15
Underground Energy Storage Potential Hungary
(ESTMAP 2016, www.estmap.eu)
5 UGS sites (•), potential for heat storage (aquifers), no potential for salt cavern storage

## Slide 16
Deep Porous Storage (fossil/renewable gases)
(depleted gas fields, deep aquifers, typically >1000m)
Natural gas (NG), bio-methane, syn-gas
Proven, Mature
Typically 4 – 40 TWh per asset
Typically seasonal (heat)
Hydrogen
Under investigation (e.g. RAG Austria)
Energy content ca. 25% compared to NG
Typically seasonal (heat), maybe electricity?
Containment, fluid-matrix reactions, purity, economy?

## Slide 17
Salt Cavern Storage (fossil/renewable gases)
(salt formations / pillars ca. 1000 – 1500 m)
Natural gas (NG), bio-methane, syn-gas
Proven, Mature
Typically 0,5 – 1 TWh per cavern
Typically peak to seasonal (heat, electricity)
Hydrogen
Proven, not mature (e.g. US)
Typically 100 – 250 GWh per cavern
Typically peak (electricity, heat, feedstock)
Compressed Air
Proven, not mature (e.g. Germany)
Typically 1 – 3 GWh per cavern
Typically peak (electricity)
Manage compression heat losses (e.g. ALACAES)

## Slide 18
Proven, not mature
40 - 120°C
0.1 – 25 GWh
Monthly to Seasonal
Integrated with district heating systems, waste heat, geothermal and agriculture heating
Large potential to manage seasonal heat demand at local level
Mid-High Temperature Heat Storage (sensible)
(shallow subsurface: ca. 0 – 500 m)
Open (aquifer)
Closed (borehole)
Lined cavity
Flooded mines

## Slide 19
Conceptual, Pilots
Typically 1 - 4 GWh
Peak / Daily (electricity)
Alternative to Surface Pumped Hydro
Cost?
Underground Pumped Hydro
(ca. 500 – 1500 m)

## Slide 20
Source: 2015 - IEA - Technology Roadmap
Family of Energy System Services
UGS

## Slide 21
Source: 2015 - IEA - Technology Roadmap
Underground
Centralized Heating and Grid Services
Family of Energy System Services
UTES
UGS
Underground
District/Greenhouse
Heat Balancing

## Slide 22
Mapping of Energy Storage Sites
Above ground / Subsurface
Existing and Future Potential
Standardized Technology KPI’s
Application in EU systems models
European Energy Storage Mapping and Planning
EC Service Contract no.: ENER/C2/2014-640/S12.698827 (www.estmap.eu)

## Slide 23
Effective valorization and implementation of large-scale underground energy storage:
Raise TRL of clean storage technologies (industry pilots, business cases, upscaling and energy-market integration)
Portfolio management: national assessments, plug & play datasets (standardized KPI’s) for energy systems modelling
Social license to operate (cost vs benefits, transparency, participation, regulatory)
Timely action (long lead times)
Serge van Gessel
Underground energy storage, Danube Region – possibilities and European perspective, Budapest, 2019.12.04

## Slide 24
Thank you for your attention
Introduction to Underground Energy Storage
European Research and Technology Perspective
Serge van Gessel
Senior Advisor Economic Affairs, TNO
Chairman Geo-Energy Expert Group EuroGeoSurveys
Serge van Gessel
Underground energy storage, Danube Region – possibilities and European perspective, Budapest, 2019.12.04